## Slide 1: Models of Computation and Communication
We need to develop a model
  to reason about the problem
  to reason about our solution
  to reason about the problem about our solution.
Models of Communication:
  OSI/ISO model (Open Systems Interconnect)
  TCP/IP model
Model of Computation: (Machine <-> Language)
  Turing Machine, Linear Bounded Automata, Pushdown Automata, and Finite State Automata
  Sequential Circuits, and Combinational Logic
  Universal Computer and Machines: Theoretical to Abstract to Physical

## Slide 3: IPv4 Packet Header

## Slide 4
OSI and TCP/IP Models
Layer | Name | Example Protocol | Naming | Transported | Hardware Device
7 | Application | http | url | data | 
6 | Presentation | --- |  |  | 
5 | Session | --- |  |  | 
4 | Transport | TCP/IP | socket | segment | 
3 | Network / Internet | IPv4/IPv6 | IP | packet | router
2 | Data Link / Link | Ethernet | MAC | frame | switch
1 | Physical | 802.11g | Interface | symbols | hub, bridge
Host layers
Media layers

## Slide 5: The Layers Simplified
Layer 1: Physical Layer
The mechanics of sending symbols -- restricted (maybe) to one's and zero's
Layer 2: Data Link
When to start and stop an individual message between two connected location
Layer 3: Network
Sending a message from A ⇒ Z by going through B to C to D to … to Y and then finally Z
Layer 4: Transport
Transmitting/Ensuring a complete message from A to Z
Address performance issues

## Slide 6: Models of Computation
Turning Machines | Recursively Enumerable | TM(Q, Σ, 𝚪, q0, 𝛅)
Linear Bounded Automata | Context Sensitive Languages | LBA(Q, Σ, 𝚪, q0, 𝛅)
Pushdown Automata | Context Free Languages | PDA(Q, Σ, 𝚪, 𝛅, q0, z0, F)
Finite State Automata | Regular Expressions | FA(Q, Σ, 𝛅, q0, F)
Sequential Circuits |  | 
Combinational Logic | Boolean Algebra | 

## Slide 7: Combinational Logic
Based upon Boolean Algebra
  all inputs and outputs restricted to True (1) and False (0)
Operations are restricted to: AND (*) , OR (+), NOT (')
Equivalent to Digital Logic, with gates:
Can be used as a building blocks:
  XOR: A ⊕ B is equivalent to (A + B) * (A' + B')
Example: Half-Adder
A | B | ⊕
False | False | False
False | True | True
True | False | True
True | True | False
java: A || B

## Slide 8: Sequential Circuits
Introduce feedback loops
Creates latch or flip-flop
  a circuit with only two stable states
Example: SR Latch
S | R | Q | Output | Description
0 | 0 | Q | Q | Hold State
0 | 1 | Q | 0 | Reset / Clear
1 | 0 | Q | 1 | Set
1 | 1 | Q | X | Not allowed: Error

## Slide 9: Finite State Machine
FA(Q, Σ, 𝛅, q0, F)
  Q = { N, W, R, B, T } // New, Waiting (Ready), Running, Blocked, Terminated
  Σ = { a, d, i, t, r, e} // admit, dispatch, interrupt, trap, resume, exit
  q0 : N
  F : { T }
  𝛅 : Q x Σ -> Q
T
N
W
R
B
a
d
i
e
t
r
FA for the Process Status Diagram
input string:
a
d
t
r
d
a
d
$
e

## Slide 10: Pushdown Automata
PDA(Q, Σ, 𝚪, 𝛅, q0, z0, F)
  Σ : set of symbols on the input string
  𝚪 : set of symbols placed on the stack
  z0: set of symbols place on the stack at startup
  𝛅 : Q x Σ x 𝚪-> Q x 𝚪*
input string:
$
Infinite Stack
C -> if ( E ) S
| if ( E ) S else S
PDA
control unit

## Slide 11: Turing Machine
TM(Q, Σ, 𝚪, 𝛅, q0)
  Σ : set of symbols on the input string
  𝚪 : set of symbols placed on the tape
    includes a blank symbol: $
  𝛅 : Q x Σ x 𝚪-> Q x 𝚪 x {R, L}
$
a
Infinite Tape
$
$
$
$
Turing Machine
input string:
$
control unit

## Slide 12: Linear Bounded Automata
Special Case of a Turing Machine
  The tape is bounded to a defined size.
h
e
l
l
o
$
$
LBA with tape size of 8
input string:
$
$
control unit

## Slide 13: Universal Computer
TM(Q, Σ, 𝚪, 𝛅, q0)
Tape: sufficiently large
A specialized control unit (aka firmware)
A specialized program placed on tape
A generic program placed on tape
Input coming from an I/O device
h
Sufficiently Large Tape
e
l
l
o
$
$
Universal Computer
input string:
$
control unit

## Slide 14: Theoretical to the Abstract
Turing Machine →
  von Neumann Architecture
  Harvard Architecture
Consider writing a Java program for these machines

## Slide 15: Physical Architecture: MIPS Microarchitecture

## Slide 16: Physical Architecture: ARM (7&9) Microarchitectures

## Slide 17: Physical Architectures: Examples

## Slide 19: Breaking things down or building them up.
Size | Network Layer | Architecture
N | data | data
MTU | segment | 
64-1522 octets | frame | 
16 bytes |  | paragraph
32 (or 64) bits | word | word
8 bits | octet | byte
4 bits | nibble | nibble
1 bit | symbol | bit